## Slide 1: OPERATIONAL SAFTEY
THINKING ABOUT BEING SAFE

## Slide 2: 1000 WAYS TO DIE
MACHINE ROLL OVER
SLIPS AND FALLS
CHAIN SHOT
SPEARS
FIRE
MECHANICAL FAILURE
OPERATOR ERROR
NOT FOLLOWING PROCEDURES
Y

## Slide 3: MACHINE ROLL OVER
CAUSES
SLOPES AND HILLS
HIGH STUMPS
OVER REACHING
MECHANICAL FAILURE
WEATHER CONDITIONS
OVER LOADING
PREVENTION
BE AWARE OF TERRAIN
WEAR YOUR SEATBELTS
KEEP STUMPS LOW
SET MACHINE UP ON THE LEVEL
BECAREFUL IN LOW VISIBILITY
KEEP BOOMS AND LOADS LOW
INSPECT MACHINE DAILY

## Slide 4
Watch Video on skidder rollover

## Slide 5: SLIPS AND FALLS
CAUSES
POOR FOOT WEAR
POOR EQUIPMENT MAINTENCE
BRUSH AND OBSTACLES
ICE/SNOW/RAIN/PITCH
PREVENTION
MAINTAIN GOOD FOOTWEAR
INSPECT EQUIPMENT DAILY FOR MISSING GRAB PADS AND STEPS
TRY TO WALK WHERE THERE IS LESS OBSTACLES
WATCH FOR ICE AND SNOW BUILD UP ON STEPS

## Slide 6: Watch Video on Professional Truck Driver Arvinds Story

## Slide 7: CHAIN SHOT
CAUSES
STRETCHED CHAINS
IMPROPER SAW SETTINGS
DAMAGED CHAINS
IMPROPER CHAIN MAINTENCE
OPERATOR ERROR
PREVENTION
CHECK FOR CHAIN STRETCH
MAINTIAN PROPER SETTINGS
CARFULLY CHECK CHAINS FOR DAMAGE PRIOR TO INTALLING
KEEP CAB OUT OF THE SHOT CONE
DON’T OVER CUT THE RAKERS

## Slide 8: Watch video on broken chain link

## Slide 9: SPEARS
CAUSES
DRIVING THROUGH UMT’S
WINDFALLS
STICKS PICKED UP IN THE TRACKS
REVERSING
SAFTEY GUARDS MISSING
PREVENTION
DON’T DRIVE OVER UMT’S CUT THEM SO THEY LAY FLAT
DON’T LEAVE LEANED OVER TREES
WATCH FOR STICKS IN THE TRACKS STOP AND REMOVE
MAKE SURE WINDSHIELDS ARE LEXAN OR GUARDED IN

## Slide 10: Watch video on Spears and skidder operators

## Slide 11: FIRE (MACHINE/FOREST)
CAUSES
POOR MACHINE MAINTENCE
CARELESS SMOKERS
MECHANICAL FAILURES
CUTTING SYSTEMS
ELECTRICAL SHORTS
PREVENTION
CLEAN ENGINE COMPARTMENT REGULARY
NO SMOKING ON JOB SITES OR IN MACHINES
REGULAR INSPECTIONS OF MACHINES
GOOD CHAIN AND SAW MAINTENCE
PROPER REAPAIRS OF WIRING SYSTEMS

## Slide 13
Watch video on Processor Fire

## Slide 14: MECHANICAL FAILURE
CAUSES
POOR EQUIPMENT MAINTENCE
OVER LOADING OF MACHINES
IMPROPER USE OF MACHINES
POOR PRETRIP INSPECTIONS
POOR EQUIPMENT DESIGNS
SEVERE WEATHER CONDITIONS
PREVENTION
PROPER MACHINE MAINTENCE
DON’T OVER LOAD THE MACHINE
USE THE MACHINE FOR ITS INTENDED USE
WATCH FOR PROBLEMS DURING PRESHIFT INSPECTIONS
COLD WEATHER FATIGUES METAL

## Slide 15: OPERATOR ERROR
CAUSES
INPROPER OPERATOR TRAINING
OPERATOR INATTENTION
OPERATOR FATIGUE
POOR COMMUNICATION
FAILURE TO KNOW THE LIMITS OF THE MACHINE
PREVENTION
DON’T OPERATE MACHINE UNLESS YOU ARE TRAINED
PAY ATTENTION TO WHAT YOU ARE DOING
LISTEN TO WHAT THE SUPERVISOR IS TELLING YOU
KNOW YOUR MACHINE AND ITS CAPABILITIES

## Slide 16: NOT FOLLOWING PROCEDURES
CAUSES
WORK ORDER NOT FOLLOWED
WORK ORDER WRITTEN IMPROPERLY
WRONG WORK ORDER FOR BLOCK
DISREGARD FOR PROCEDURES
COMPLACENCY
PREVENTION
FOLLOW YOUR WORK ORDER
IF THE WORK ORDER SEEMS WRONG ASK SUPERVISOR
MAKE SURE WORK ORDER IS FOR BLOCK IN QUESTION
FOLLOW THE PROCEDURES
TO BE COMPLACENT IS TO DIE

## Slide 17: THESE WERE JUST A FEW WAYS TO GET HURT OR KILLED
THERE ARE MANY MANY MORE

## Slide 18: A FEW OTHER THINGS TO THINK ABOUT
THERE IS NO END TO SAFTEY

## Slide 19: EMERGENCY EVACUATION
DON’T THINK YOU WON’T NEED IT

## Slide 20: Watch Forestry ERP video

## Slide 21
EMERGENCY EVACUATION PLAN
In the event of an emergency the civic address to give to the 911 operator is 446 Tay Falls Road, Woodlands N.B.
The emergency meeting point at the 446 sign where the block road meets the Tay Falls Road
Emergency numbers:
911 FIRE, Ambulance, Police
Jeremy Jones 506 261 0827 Lead instructor
Kyle O’shea 506 626 2479 NBCC
Loisanne Gregan 506 778 6054 NBCC

## Slide 22: YES SAFTEY IS EVERYONE’S RESPONSIBILITY
HOWEVER ITS YOUR LIFE SO WORK RESPONSIBLY